## Slide 1
Environmental module
draft
Nunzio SARNINO and Subhasish BASAK
Lucie COLLINEAU

## Slide 2: General framework

## Slide 3: Computation of risk
Quantity of interest : For a particular broiler flock raised at a farm characterized by production parameters Ɵfarm, we want to estimate the risk or the probability of getting ESBL E. coli carriership for a human being exposed through one of the environmental subpathways that are treated with contaminated poultry manure coming form that farm.
Manure
Ground water
Surface water
Recreational swimming
Fresh produce
Soil
Tap water
Human exposure

## Slide 4: Computation of risk
Manure
Ground water
Surface water
Recreational swimming
Fresh produce
Soil
Tap water
1
3
2
SWAT
Quantity of interest : For a particular broiler flock raised at a farm characterized by production parameters Ɵfarm, we want to estimate the risk or the probability of getting ESBL E. coli carriership for a human being exposed through one of the environmental subpathways that are treated with contaminated poultry manure coming form that farm.
Human exposure

## Slide 5: Framework
SWAT
Module assumptions:
The manure is applied once to the agricultural field, that eventually contaminates the surface water (lake)
The concentration of ESBL E. coli in the watershed is estimated using a SWAT model
Manure
Surface water
Recreational swimming
Fresh produce
Tap water
Human exposure
Cmanure
Cinit
Cmanure (in CFU/g)  Cinit (in CFU/ml)

## Slide 6: Framework
Module assumptions:
The manure is applied once to the agricultural field, that eventually contaminates the surface water (lake)
The concentration of ESBL E. coli in the watershed is estimated using a SWAT model
SWAT model for a particular geographical region :
Identifies the waterbody and the adjacent agricultural land
Uses the data:
  Digital Elevation Model (DEM) : A 3D representation of the land providing a digital approximation of the Earth's topography
  Land Use and Land Cover (LULC) data : Types of land use (e.g., agriculture, urban) and the physical surface cover (e.g., forests, grasslands)
  Soil Data : Texture, depth, and hydraulic properties
  Weather Data : Historical data (precipitation, temp., wind speed, humidity etc.)
  Manure Application Data : Timings, protocols and methods
  Water Quality Data
The SWAT model initializes
  DEMs to define the waterbodies of interests and sub-basins
  Next Hydrological Response Units (HRUs) needs to be define that combine land use, soil type, and slope classes for each sub-basin
  Then the model is fed with the climate and environmental data

## Slide 7: Bacteria transportation from soil to watershed Neitsch et al. (2011)
2:3.1 SOIL STRUCTURE
Soil is comprised of three phases—solid, liquid and gas. The solid phase consists of minerals and/or organic matter that forms the matrix or skeleton of the soil. Between the solid particles, soil pores are formed that hold the liquid and gas phases. The soil solution may fill the soil pores completely (saturated) or partially (unsaturated).
0.2.1 The hydrologic cycle as simulated by SWAT is based on the water balance equation
SURFACE RUNOFF (Q_surf)
Surface runoff, or overland flow, is flow that occurs along a sloping surface. Using daily or subdaily rainfall amounts, SWAT simulates surface runoff volumes and peak runoff rates for each HRU. SURFACE RUNOFF VOLUME is computed using a modification of the SCS curve number method (USDA Soil Conservation Service, 1972) .
4:4.1.2 bacteria (from soil solution) transported in surface runoff 4:4.2.2 bacteria (attached to sediments) transported in surface runoff 4:4.3 In large subbasins with a time of concentration greater than 1 day, only a portion of the surface runoff will reach the main channel on the day it is generated. The time of concentration (Tc) refers to the time it takes for water to travel from the most distant point in a HRU to watershed.

## Slide 8: Environmental decay
SWAT
Following O’Flaherty et al. (2019) the ESBL E. coli decays in the water and the decay rate depends on environmental parameters.
Mancini’s equation is used to compute the decay rate k
For each submodule the conc. Cwater(d) (in CFU/ml) is computed at timepoint d (in days) when the water is used
Manure
Surface water
Recreational swimming
Fresh produce
Tap water
Human exposure
Cmanure
Cinit
Cdecay(dharvest)
Cdecay(dswim)
Cdecay(dDWTP)
dharvest = 1, 2, …, nharvest days (nharvest = 14)
dswim = time between contamination and swimming ?
dDWTP = time to reach DWTP ~ 1-10 mins
Cwater(d) = Cinit . exp(-kd)

## Slide 9: Tap water consumption

## Slide 10: Drinking Water Treatement Plant
Following O’Flaherty et al. (2018) different DWT protocols are implemented
After treatement concentation CDWTP is estimated for each protocol
Cwater (in CFU/ml)  CDWTP (in CFU/ml)
SWAT
Manure
Surface water
DWTP
Human exposure (in CFU)
Cmanure
Cinit
Cdecay(dDWTP)
Decay
CDWTP
CDWTP x Wconsum

## Slide 11: Recreational swimming

## Slide 12: Accidental ingestion while swimming
Following O’Flaherty et al. (2019)
Concentation Cbath is estimated for bathing area
Cwater (in CFU/ml)  Cbath (in CFU/ml)
SWAT
Manure
Surface water
Bathing site
Human exposure (in CFU)
Cmanure
Cinit
Decay
Cbath
Cbath x Wingest
Cdecay(dswim)
Assume worst case scenario with dswim = 0
Wingest for an hour of swimming

## Slide 13: Consuming lettuce

## Slide 14: Contamination of lettuce
Irrigation
Irrigation
Following O’Flaherty et al. (2019)
Irrigation is done daily with water conc. Cwater(dharvest), for dharvest = 1, 2, …, nharvest days (nharvest = 14)
SWAT
Manure
Surface water
Irrigation
Cmanure
Cinit
Decay
Cdecay(dharvest)
Irrigation
2
1
3
nharvest
Lettuce
Cummulative O’Flaherty et al. (2019) accumulation + decay
Clettuce
Cadhesion(dharvest) in CFU/g
Cadhesion(dharvest) = Cdecay(dharvest) x Wattach
Decay
Decay
Decay
2
3
nharvest
Decay
1
Pdecay(dharvest)
Pdecay(t) = f . exp(-k1.t) + (1-f) . exp(-k2.t)
Survial proportion on timepoint t McKellar et al. (2014)
Clettuce = Ʃdharvest Cadhesion(dharvest) . Pdecay(nharvest – dharvest + 1)
in CFU/g

## Slide 15: Postharvest processing of lettuce
Following O’Flaherty et al. (2019)
Lettuce
Clettuce
Postharvest treatment
Clettuce.post
Consumer wasing
Clettuce.wash
Human exposure (in CFU)
Clettuce.consum x Lconsum
Clettuce.post X (1 - rwash)
rwash ~ Triangular(0.65, 0.99, 0.99)
Washing with water
Consumption before expiry
De Giusti et al. (2010)